## Slide 1: Efficiency of model rockets
T.S. Sriram

## Slide 2: What is Efficiency
Efficiency is the ratio of the useful work done to the energy expended.
In the case of the model rocket, we expend energy by burning black powder – this causes gases exiting the nozzle at a high velocity, which in turn propels the rocket.

## Slide 3: Steps to calculating efficiency
Figure out energy produced by the reaction for a known mass of reactants
Figure out energy required to expel a known mass of reaction products (gases and solids) at a known exhaust velocity
  Assumptions
    All of the black powder is consumed
    Both the solid and gaseous reaction products are expelled through the nozzle
Calculate the ratio

## Slide 4: Figuring out the energy produced by reaction
Black powder reaction:
  2 KNO3 + S + 3 C → K2S + N2 + 3 CO2 + 571.7kilojoules*
571.7 KJ is the energy produced per mole of reactants
  We need to figure out how much energy is produced by 21.1 g of reactants
  How many grams is 1 mole of reactants
    Add up all the atomic weights on the right side of the reaction:
      2*(39 +14+3*16) + 32 + 3*12 = 270 g = 1 mole of reactants
      Energy produced by 21.1 g = (21.1/270)*571.7 = 44.7 kilojoules
*Can obtain this by subtracting standard enthalpies of formation of the product side and
the reactant side. Standard enthalpies of formation can be obtained from the CRC handbook
Of Chemistry and Physics. This is a simplified version of the reaction.

## Slide 5: Calculating energy needed to accelerate the reaction products
Mass of reaction products consumed = 21.1g = 0.0211 kg(from Estes D12 datasheet)
Exhaust velocity = total impulse/mass consumed = 16.84 N-sec/0.0211 kg = 798.1 m/sec
Kinetic energy of exhaust = ½ mV2 = ½ *0.02111*798.1^2 =6720.04 joules = 6.72 kJ

## Slide 6: Efficiency
Work done to accelerate the exhaust = 6.72 kJ
Energy produced by burning 21.1g of black powder = 44.7 kJ
Efficiency = 6.72/44.7 = 0.1503 = 15.03%